DEPARTMENT OF INDUSTRIAL ENGINEERING AND MANAGEMENT

DAWOOD COLLEGE OF ENGINEERING & TECHNOLOGY, KARACHI

Assignment # 02

Date of Assignment Issue: 06.12.12					Date of Submission: 20.12.12

Subject: Management of Engineering Projects (Theory)

Batch/Term: 2010/ 6th 							           Max Marks: 10

Note:	a. Answer All the Questions

b. Format of Write up:  Hand written report

Q#1. Enlist the possible types of investment Criterion & Discuss NPV & its Properties

Q#2. Calculate the NPV of the project with cash flows given below. When the cost of capital is 14%. Also suggest the viability of such project

| Year | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Cash flow | (1,000,000) | 200,000 | 200,000 | 300,000 | 300,000 | 350,00 | 250,000 | 150,000 | 90,000 |

Q#3. Define BCR & NBCR. Write Similar & Dissimilar properties BCR & NPV.

Q#4. Estimate the BCR & NBCR of the project with cash flows given below. When the cost of capital is 14%. Also suggest the viability of such project in guidelines of BCR & NBCR

| Year | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Cash flow | (100,000) | 20,000 | 20,000 | 30,000 | 30,000 | 35,000 | 25,000 | 15,000 | 9,000 |

Q#5. Estimate The modified NPV for the two projects X & Y, the cash flows for each as given below. The two re-investment rates for each project are 15% & 21%. Assume the cost of capital as 11%

|  | Year | 0 | 1 | 2 | 3 | 4 | 5 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Project: X | Cash flow | (110,00) | 31,000 | 40,000 | 50,000 | 70,000 | 35,000 |
| Project: Y | Cash flow | (110,00) | 71,000 | 40,000 | 40,000 | 20,000 | 30,000 |

Q#6. Define & Express Mathematically the Internal Rate of Return & Modified IRR. What these suggest in the investment analysis

Q#7. Estimate the exact value of IRR for the following project data

| Year | 0 | 1 | 2 | 3 | 4 | 5 |
| --- | --- | --- | --- | --- | --- | --- |
| Cash flow | (1,000,00) | 30,000 | 40,000 | 45,000 | 50,000 | 55,000 |

Q#08. Estimate the value of MIRR for the following project data. Assume cost of capital as 17%

| Year | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Cash flow | (120) | (80) | (55) | 20 | 60 | 80 | 100 | 120 |

Q#09. (a). Enlist all Measures for Accounting Rate of Return

(b). Find the discounted payback period on following project data, when the cost of

capital is 10%

| Year | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Cash flow | 10000 | 3000 | 3500 | 4000 | 4200 | 4500 | 4800 | 4900 |

Q#10. Write short note on two of the following

- Urgency

- Modified NPV

- Conventional & Non-conventional Projects

-The End-