## Slide 1: PRODUCTION SYSTEMS
Terminology Concept:
Production:
  It refers to rate of production in terms of machine, labor, material, or any other effective basis
  The act or process of producing
Performance:
  = Actual achievement in effective work done x 100/
  An ideal or basic standard target of achievment

## Slide 2: PRODUCTION SYSTEMS
Terminology Concept: (Cont..)
Productivity:
= Out/Input
System:
- A group of interrelated parts or elements
designed to achieve a particular goal or,
- A group of units so combined as to form a
whole & to operate in unison

## Slide 3: PRODUCTION SYSTEMS
Terminology Concept: (cont..)
Design:
- It is an activity to convert the resources into
systems economically to meet the human needs
- To conceive and plan out in mind
- To devise for a specific function or end
- To make a pattern or sketch
6. System Design:
It refers to the design of a collection of components through the conceptual modeling

## Slide 4: PRODUCTION SYSTEMS CLASSIFICATION:
Classification is made according to the arrangement of machines & departments within the mfg plants

## Slide 5: PRODUCTION SYSTEMS CLASSIFICATION:
 | Project | Job Shop | Repetitive | Line | Continuous
Process Speed | Varies | Slow | Moderate | Fast | Very fast
Labor content | High | High | Medium | Low | Very low
Labor skill level | High | High | Moderate | Low | Varies
Order Quantity | Very small | Low | Varies | High | Very High
Unit Quantity Cost | Very High | Large | Moderate | Low | Very low
Routing Variations | Very High | High | None | Low | Very low
Product Options/Product Variety | Low | Very High | High | low | Very low
Design component | Very Large | Large | Very Small | Moderate | Small

## Slide 6: PRODUCTION SYSTEMS CLASSIFICATION:
Project:
The most distinguishing characteristic of project category is that products are complex, with many parts, & are most often one of a kind.
Eg. Project type companies build oil refineries, large office buildings, cruise ships
In each case, products may be similar but usually are not identical
They use the fixed position type layout
Customer is identified before production starts

## Slide 7: PRODUCTION SYSTEMS CLASSIFICATION:
2. Job Shop:
It is suitable for companies which produce in low Volume many different products
It require general purpose equipment & m/cs, highly skilled labor, general purpose tooling & fixtures
Similar m/cs can be grouped together within the plant to form a department
It has minimum automation
It attains high degree of flexibility to produce in variety
It is very responsive to changes in the market
It uses job shop or Process layout
It is observed that about 30-50% of mfg systems in USA are of Job Shop
Egs: manufacture of large Turbogenerators, Hydrogenerators

## Slide 8: PRODUCTION SYSTEMS CLASSIFICATION:
2. Job Shop: (cont..)
Problems Associated:
Expense associated with variety of tool & fixture is large
achieving machine-load balancing is difficult
Material handling excessive bcz one might pass through the same department many times
Each item or batch of the parts requires its own production shop orders, which can result in excessive book keeping
Excessive setup times

## Slide 9: PRODUCTION SYSTEMS CLASSIFICATION:
Batch Production:
It falls b/w a job shop & an assembly line in its complexity
It is suitable for the firms which produce intermediate quantities with intermediate variety
Products are manufactured in batches bcz the production capacity almost is higher than the demand for product
It uses some what specialized & high speed m/c tools & eqpts
eg: manufacturers of furniture, appliances, & mobile homes
It uses Process layout

## Slide 10: PRODUCTION SYSTEMS CLASSIFICATION:
Mass Production:
is used for high volume & single (minimum) variety production
Eqpts used are very specialized & fast
Investment in special tools, jigs & fixtures is very large
The work content are broken down into many small groups & over all labor skills required are minimized
Productivity is very high & is achieved to great extent by automation
Output rate is controlled by the design of Lines (Stations) & / or the manpower assigned to these stations
The periodic review of inventory may suggest changes in output rate

## Slide 11: PRODUCTION SYSTEMS CLASSIFICATION:
Mass Production: (cont..)
It further classifies into:
  a. Assembly Line Mass Production System:
  It used to produce a discrete product
  Typically, partial subassemblies are moved from one workstation to the next in sequence by a fast moving material handling system (eg. Conveyer belts) past each station, advancing the product to its final assembly
  Travel of assembly within the station is continuous or intermittent depending on nature of job to be performed
  The total work for a job is distributed among the work stations that form the assembly line such that complete their assigned tasks in approximately the same time (also called cycle time)
  Eg: Automobile manufacture

## Slide 12: PRODUCTION SYSTEMS CLASSIFICATION:
4. Mass Production: (cont..)
It further classifies into:
  b. Flow Line Mass Production System:
  - Is used to describe a continuous production process, such that of chemicals, liquids & gaseous products, & paper as well as die operation such as wire mfg.